The specifier will need to edit this product specification for a specific project to reflect the options and applications being used.  This guide section has been written to show items to be determined reflected in italic red.  America’s Gate Company does not warrant that these specifications are complete and applicable to all applications.  It is the specifier’s responsibility to assure that use of these specifications is an appropriate fit for the site and conditions.

SECTION 02830 Ornamental Cantilever Gate

PART 1 - GENERAL

  - SECTION INCLUDES:

    - The work in this section shall include furnishing all labor, materials, equipment and appliances necessary to complete all cantilever slide gate(s) required for this project in strict accordance with this specification section and drawings.

  - REFERENCES:

    - Underwriters Laboratory Gate Operator Requirements (UL 325).  See 3.02 C.

      - Automated/operated vehicular gates are not to be used for pedestrian traffic.  Separate pedestrian gates must always be provided if pedestrian traffic is expected.

## ASTM F 2200 – Standard Specification for Automated Vehicular Gate Construction.  See 2.01 C.

## ASTM F 1184 – Standard Specification for Industrial and Commercial Horizontal Slide Gates, Type II, Class 2.  See 3.02 B.

## American Welding Society AWS D1.2 Structural Welding Code.  See 2.01 D and 2.03 D.

  - SUBMITTAL:

    - Product Data:

      - Provide manufacturer’s catalog cuts with printed specifications and installation instructions.

      - If operated gate system, furnish two (2) copies of operation and maintenance data covering the installed products.

    - Shop Drawings:

      - Supply shop drawings showing the gate system, including details of all major components.

      - Include details of gate construction, gate height, and post spacing dimensions.

    - Certification of Performance Criteria:

      - Manufacturer of gate system shall provide certification stating the gate system includes the following material components that provide superior performance and longevity. Alternate designs built to minimum standards that do not include these additional structural features shall not be accepted.

        - Gate shall have a minimum counterbalance length of 50% opening width which provides a 36% increase in lateral resistance (when compared to ASTM minimum of 40% counterbalance). If gate is ever to be automated, counterbalance section shall be filled with fabric or other specified material.

        - Entire gate frame (including counterbalance section) shall include 2 adjustable stainless or galvanized steel cables (minimum 3/16”) per bay to allow complete gate frame adjustment (maintaining strongest structural square and level orientation).

        - Gate truck assemblies shall be tested for continuous duty and shall have precision ground and hardened components.  Bearings shall be pre-lubricated and contain shock resistant outer races and captured seals.

        - Gate truck assemblies shall be supported by a minimum 5/8” plated steel bolt with self aligning capability, rated to support a 2,000 # reaction load.

        - Hanger brackets shall be hot dipped galvanized steel with a minimum 3/8” thickness.

    - Certifications:

      - Gate in compliance with ASTM F 2200, Standard Specification for Automated Vehicular Gate Construction per section 2.01 C.

      - If operated gate system, gate operator shall be in compliance with UL 325 as evidenced by UL listing label attached to gate operator.

      - The aluminum welders and welding process must be certified per section 2.03 D.

      - Manufacturer shall supply gate design performance certification.

- PRODUCTS:

  - CANTILEVER SLIDE GATE MANUFACTURERS:

    - The cantilever sliding gate system shall be manufactured by America’s Gate Company, 12330 Cary Circle La Vista NE 68128

    - Approved substitution – All other systems must be submitted to the design team in accordance with substitution requirements as set forth in the general provisions of the specification manual for approval prior to the bid date.  Products submitted must meet performance criteria. Products submitted after the bid date will not be approved.

    - Gate manufacturer shall certify gate is manufactured in compliance with                   ASTM F 2200, Standard Specification for Automated Vehicular Gate Construction.  See 1.03 D.1.

    - Upon request, gate manufacturer shall provide independent certification as to the use of a documented Welding Procedure Specification and Procedure Qualification Record to insure conformance to the AWS D1.2 welding code.  Upon request, Individual Certificates of Welder Qualification documenting successful completion of the requirements of the AWS D1.2 code shall also be provided.

  - ESTATE GATE CONSTRUCTION

    - Horizontal members:  The gate frame shall be fabricated from 6063-T6 aluminum alloy extrusions.  The top member(s) shall be a 2” x 1” x .577 lb/ft. aluminum structural channel.  The channel(s) shall be machined rolled without deformity, dimples, crimps or roller marks to the radius shown on the drawings.  Each leaf rail will consist of two opposing radius as shown on the drawings.  The bottom member shall be a 2” x 2"  aluminum structural tube weighing not less than 1.6 lb/ft..

    - Vertical Members:The vertical members at the ends of the opening portion of the frame shall be 2” x 2” (51mm x 51mm) in the cross section weighing not less than 1.1 lb/lf (1.6kg/m).

    - Ornamental picket infill:  The gate shall be completed by installation of ornamental pickets.  Picket sizes shall be 1” x 1x .275 lb/ft.  or ¾” x ¾” x .201 lb/ft.  Pickets will extend through entire length of the gate panel as shown on the drawings.  Picket caps will be adorned as shown on the drawings.

    - All welds on the gate frame shall conform to Welding Procedure Specification and Procedure Qualification Record to insure conformance to the AWS D1.2Structural Welding Code.  All individual welders shall be certified to AWS D1.2 welding code.

    - Each gate leaf shall be provided with a minimum of two pivoting hinges to allow proper operation, and shall be connected to the gate side of the hinge by means of two through-bolts.

  - CANTILEVER GATE CONSTRUCTION DETAILS:

## Top Track:  The frame(s) and track(s) are to be fabricated from aluminum extrusions (6061-T6).  Single track applications provide an upper track that weighs 5.15# / foot.  Double track applications provide an upper track that weighs 11.916# / ft.

## Vertical Uprights: The vertical uprights shall be a minimum of 2” x 2” x 1.12#/ foot (6063-T6) aluminum extrusions.

## Diagonal Bracing.  Diagonal "X" bracing of 3/16" or 1/4” diameter stainless or galvanized steel cable shall be installed throughout the entire gate frame.

## Bottom Track:  The bottom track shall be a minimum of 2” x 2” x 1.12#/ foot (6063-T6) aluminum extrusions.  For openings greater than 25’, the bottom track shall be a minimum of 2” x 5” x 3.12# / foot.

    - Ornamental Picket:  Picket sizes shall be 1” square .509#/ foot or ¾” square .364#/foot (6063-T52) aluminum extrusions. Picket size and design should best match adjoining ornamental fence and as shown.  Pickets may extend through only the clear opening portion or through the entire length of the gate as required.  If a motorized gate operator is to be applied to the gate and the specified picket spacing allows for openings in the gate frame that exceed 2¼” (57mm), a secondary gate filler shall be secured at each end of the gate frame and tied at each 1” x 2” (25mm x 51mm) or 2” x 2” (51mm x 51mm) vertical member.  The secondary gate filler shall extend to a minimum height of 72” (1.2m) above grade and shall be sized to prevent a 2¼” (57mm) diameter sphere from passing through openings anywhere along the length of the gate frame, and in that portion of the adjacent fence that the gate covers in the open position.

## All welds on the gate frame shall conform to Welding Procedure Specification and Procedure Qualification Record to insure conformance to the AWS D1.2 Structural Welding Code.  All individual welders shall be certified to AWS D1.2 welding code.  See 1.02 D.

## Gate Mounting:

      - The gate frame is to be supported from the track by two (2) swivel type, self-aligning, 4-wheeled, sealed lubricant, ball-bearing truck assemblies.

      - The bottom of each support post shall have a bracket equipped with a pair of 3” (76mm) UHMW guide wheels Wheel cover protectors shall be included with bottom guides to comply with UL325.

      - Gap protectors shall be provided and installed, compliant with ASTM F 2200-05.

## The gate shall be completed by installation of approved filler as specified.

  - POSTS:

## A single set of support posts shall be minimum 4" O.D. (102mm) round SS40 or 4” x 4” x 3/16” wall square steel tubing, grade 500.  Gate posts shall be galvanized or coated and supported in concrete footings as specified by the design team.

  - FINISH:

## Gate to be mill finish aluminum or color coated with polyester powder as specified. If powder coated, the gate (including track member) and all accessories shall be pretreated chemically by sand blasting or other acceptable method to ensure proper coating adherence.

  - WARRANTY:

## The truck assembly shall be warranted against manufacturing defects by the manufacturer for a period of (5) five years from date of sale.

- EXECUTION:

  - Final grades and installation conditions shall be examined.  Installation shall not begin until all unsatisfactory conditions are corrected.

  - INSTALLATION:

    - Equipment in this section shall be installed in strict accordance with the company’s printed instructions unless otherwise shown on the contract drawings.

    - The gate and installation shall conform to ASTM F 1184 standards for aluminum cantilever slide gates, Type II, Class 2.  See 1.02 C.

    - If the gate system is to be automated, the gate and installation shall also comply with ASTM F 2200 and UL 325.  See 1.02 A and 1.02 B..

  - SYSTEM VALIDATION:

    - The complete system shall be adjusted to assure it is performing properly.

    - The system shall be operated for a sufficient period of time to determine that the system is in proper working order.

    - For operated gate systems - test and explain safety features:

### Each system feature and device is a separate component of the gate system.

### Read and follow all instructions for each component.

### Ensure that all instructions for mechanical components, safety devices and the gate operator are available for everyone who will be using the gate system.

### The warning signs shipped with the gate operator must be installed in prominent position on both sides of the gate.

### Ensure the owner is clear with regard to the safety points concerning the basic operational guidelines of the safety features of the gate operator system.  These safety points are listed in the gate operator manual and must be read prior to system use.

Note:  America’s Gate Company reserves the right to modify and/or make changes as deemed necessary without previous notice.